PEM Insert Best Practices

M5 – Hole Size (diameter/radius)

Material	Orientation
	In top (normal to bed)	In side (parallel to bed)
ABS	7.4mm/3.7mm	7.6mm/3.8mm
PLA	7.6mm/3.8mm	7.8mm/3.9mm
PC-MAX

M3 – Hole Size (diameter/radius)

Material	Orientation
	In top (normal to bed)	In side (parallel to bed)
ABS	4.4mm/2.2mm	4.4mm/2.2mm
PLA	4.6mm/2.3mm	4.2mm/2.1mm
PC-MAX

PENN Engineering Specs:
http://www.pemnet.com/fastening_products/pdf/sidata.pdf
M5/ABS (molded): Pullout – 1710N, Torque-out – 6.1 N*m
M3/ABS (molded): Pullout – 730N, Torque-out – 1.58 N*m